## Slide 1: ArduCAM Mini 2MP with ESP8266 NodeMCU
Prepared by Suk Jin Lee

## Slide 2: What is ArduCAM
ArduCAM is an open-source project for Arduino camera since back to 2012.
It is the world’s first serial peripheral interface (SPI) camera for Arduino and fills the gap of missing camera support in Arduino ecosystem.

## Slide 3: NodeMCU ESP8266
ESP8266 Wi-Fi transceiver module
  An open-source firmware and development kit that helps you to prototype or build IoT products.
  Compatible with the 802.11 b/g/n standard at 2.4 GHz
Cost-effective IoT Solution with Arduino
  Arduino is widely used cost-effective open-source development platform for embedded and IoT applications.
  Arduino IDE is extremely friendly to all users, including the new starters.

## Slide 4: Microcontroller to Raspberry Pi (1)
Microcontroller to Raspberry Pi Wi-Fi Communication
ESP8266 Wi-Fi
ArduCAM mini 2MP with ESP8266 nodeMCU
Desktop/Laptop
Stream Server
(ArduCAM mini 2MP)
Access Point
(Raspberry Pi)
http protocol
USB
Local Network

## Slide 5: Microcontroller to Raspberry Pi (2)
Microcontroller to Raspberry Pi Wi-Fi Communication
Access Point
(Raspberry Pi)
Stream Server
(IP: 192.168.4.6)
Dynamic (dhcp)
Access Point
(wlan0: 192.168.4.1)
static
SSID, PASSWORD
Wi-Fi Mode = Station Mode(0) or Access Point Mode (1)
Stream Server
(ArduCAM mini 2MP)

## Slide 6: NodeMCU to ArduCAM Mini 2MP
Wiring between NodeMCU and ArduCAM Mini 2MP
Be careful. Faulty Wiring can Lead to Fire Hazards~!
ArduCAM Mini 2MP | ESP8266 NodeMCU
CS | D0
MOSI | D7
MISO | D6
SCK | D5
GND | GND
VCC | 3V3
SDA | D2
SCL | D1
Notes: https://forum.arducam.com/t/some-questions-about-arducam-mini-2mp-plus-with-nodemcu-v3/1011/3

## Slide 7: Installation Instructions (1)
Install the current upstream Arduino IDE at the 1.8 level or later.
Notes: Run the Install Script: https://docs.arduino.cc/software/ide-v1/tutorials/Linux/

## Slide 8: Installation Instructions (2)
Install Arduino IDE using APT Manager
    sudo apt update
    sudo apt install arduino
    sudo arduino
Start Arduino
Open Preferences window and include additional Boards Manager URLs:
    http://www.arducam.com/downloads/ESP8266_UNO/package_ArduCAM_index.json
    https://dl.espressif.com/dl/package_esp32_index.json
    http://arduino.esp8266.com/stable/package_esp8266com_index.json

## Slide 11: Installation Instructions (3)
Open Boards Manager from Tools > Board menu and install esp8266 platform

## Slide 12: Installation Instructions (4)
Open Manage Libraries: Sketch > Include Library > Manage Libraries and install ArduCAM

## Slide 13: Quickly Run the Demo (1)
ArduCAM_ESP8266_UNO.ino
  https://www.arducam.com/arducam-supports-esp8266-arduino-board-wifi-websocket-camera-demo/

## Slide 14: Quickly Run the Demo (2)
Set “SSID” and “PASSWORD.”
Set Wi-Fi Mode: wifi_mode = 0 (station mode)

## Slide 15: Quickly Run the Demo (3)
Select a board:
  Tools >Board > ESP8266 Boards > NodeMCU 1.0 (ESP-12E Module)
Click “Verify” and “Upload.”

## Slide 16: Serial Monitor
After compiling and uploading the file, you can check the status using the serial monitor.
  Set baud rate: 115200 baud
Make sure that your nodeMCU connected to RPi and the server started (e.g., IP: 192.168.4.6).
Streaming server IP

## Slide 17: Access to the Server (1)
Click “web Browser” in your raspberry pi.
Type the IP of Stream Server: 192.168.4.6/stream
The capture and streaming features can be reached directly via the browser by using the format:
  For still capture: http://IPaddress/capture
  For streaming video: http://IPaddress/stream

## Slide 18: Access to the Server (2)
Click “web Browser” from your smartphone.
Type the IP of Stream Server: 192.168.4.6/stream